## Slide 1
Jubcor Presentation
Innovative Real-Time Pit Detection and Artificial Intelligence Electrical Resistance Corrosion Monitoring Systems
NEXCORR, USA
Presented By: Cheolho Kang (CK)
JUBCOR
CONFERENCE & EXHIBITION
2024
INNOVATIVE SOLUTIONS FOR CORROSION CHALLENGES

## Slide 2
Introduction
Innovative Internal Corrosion Monitoring Systems
  Artificial Intelligence Electrical Resistance (i-ER)
  Pit Detection System (PDS)
  PDS + i-ER (MFS)
Comparison Results
Conclusions
Outlines

## Slide 3
Importance of Corrosion Monitoring
For a safe and efficient operation of pipelines, corrosion must be monitored.
Functions of corrosion monitoring
  Detection of corrosion problems
  Control of the effectiveness of the corrosion protection (inhibition protection)
  Estimation of the inspection/maintenance requirements
  Estimation of the useful service life

## Slide 4
Corrosion Monitoring Techniques
Classification based on the physical principles of the technique:
  Metal Loss Techniques:
    Weight-loss Coupons, Electrical Resistance (ER)
  Electrochemical Techniques
    LPR, EIS, ECN
  Ultrasound
  FSM
Courtesy by Metal Samples

## Slide 5
Weight-Loss Coupon Technique
ADVANTAGES
Relatively inexpensive
Simple to use
Usable in any environmental Conditions
Suitable for the detection of localized corrosion.
DISADVANTAGES
Integrates corrosion over period of exposure.
High corrosion rates for short periods of time cannot be detectable.
The effects of corrosion dynamics can not be isolated.
Cannot be used for continuous in-situ monitoring.
Measurement requires long exposure time (90 days).
Pitting Corrosion

## Slide 6
Electrical Resistance (ER) Technique
ADVANTAGES
Can be used in any environment.
Changes in corrosion rate can be detected.
Continuous monitoring is possible.
Much faster response than coupons.
DISADVANTAGES
Element life is inversely proportional to sensitivity.
Conductive deposits (e.g. iron sulfide or carbonaceous material) on the sensor elements obviously distort the readings for corrosion rate.
Sensitive to dynamic temperature changes
Not suitable for the detection of localized corrosion.
Uniform Corrosion
Pitting Corrosion

## Slide 7
Cutting-Edge Technology:
Innovative Corrosion Monitoring Systems
Internal corrosion monitoring systems for the detection of real-time
pitting corrosion (Patented Technology).
Artificial Intelligence (AI) Electrical Resistance Corrosion
Monitoring System (i-ER)
Pit Detection Corrosion Monitoring System (PDS)
Multi-functional Corrosion Monitoring System (MFS: PDS + i-ER)
Uniform (General) Corrosion
Pitting Corrosion
I - ER
MFS
PDS

## Slide 8
i – ER (Electrical Resistance) System
Artificial Intelligence (AI) Electrical Resistance Corrosion
Monitoring System (i-ER)
The most relevant data point for metal loss is displayed by the Linear Regression Technique after 100 data points per time interval set up for each data collection are analyzed using an AI algorithms.
The reliability of ER data was improved using the analysis technique of an artificial neural network.
i-ER system can be upgraded periodically from the data collection of oil/gas fields using Artificial Neural Network sand AI algorithms.
A high-sensitivity, flush-mounted type ER probe.

## Slide 9
Pit Detection System (PDS): USA Patent Pending
The PDS has three (3) carbon steel layers of each 40 µm) thickness.
The probe has carbon steel layers.
In between each layer, there is a thin film which dissolves as soon as layer penetration occurs.
Each layer in the probe has a set voltage value, and the
voltage source is connected to a circuit in the transmitter.
Thin film is applied to each layer by semiconductor
processing-based technology.
Advantages of PDS:
Usable in any environmental conditions
No modification of the port is necessary because the pit detection probe can be installed at the “existing port for ER or weight loss coupon”.
Real - time pit detection monitoring
Pit penetration rate can be easily calculated.
Any change of field conditions during the monitoring does not have any problem.
40 µm
40 µm
40 µm
First Pitting
Second Pitting
Third Pitting

## Slide 10
Multi-functional System (MFS): USA Patent Pending
MFS: Combination of PDS + i-ER
Advantages:
Usable in any environmental conditions
No modification of the port is necessary because MFS probe can be installed at the “existing port for ER or weight loss coupon”.
Real-time pit detection and general corrosion rate monitoring
The pit penetration rate can be easily monitored.
Any change in field conditions during the monitoring does not have any problems.
The multi-functional Probe System (MFS) can monitor pit detection using PDS (pit detection) and general corrosion rates using electrical resistance (i-ER).

## Slide 11
Transmitter
The all-in-one transmitter was designed to use PDS, i-ER, and MFS.
The high-resolution transmitter has a self-diagnosis function regarding abnormal voltage and temperature.
Transmitter electricity sensor: overvoltage/low-voltage detection and error signal
Transmitter temperature sensor: temperature monitoring and error signal
Transmitter temperature sensor: temperature monitoring and error signal
The software will show a reset message if the transmitter needs to reset
due to a problem. This will lead to reliable PDS, i-ER, and MFS data
collection.
Heat shield Protection: The transmitter can withstand rapid changes in external temperature up to 70C.
Transmitter

## Slide 12
Transmitter Heat shield Protection:

## Slide 13
Software
User-friendly software
All-in-one software for PDS, MFS and i-ER
Software is designed to detect the type probe (PDS, i-ER and MFS) automatically. No manual input is necessary.
Warning signal with pitting corrosion
ER probe life signal
Software will be periodically upgraded using AI according to ER and weight-loss coupon data collection.

## Slide 14
Portable Data Logger
Tablet-type portable data logger to collect data from PDS, i-ER and MFS.
Features
Firmware Tablet
Automatic data collection and stored data
Easy data transfer to PC
Display system map
Corrosion rate results and graph display on Tablet
High-resolution, rapid response
Easy to upgrade a software
Multilingual capability
Industrial Tablet

## Slide 15
Test Results of i-ER
Multiphase Flow, Corrosion Loop System
Weight-Loss Coupon
i-ER
(Courtesy by Unicoh Specialty Chemicals)
Parameter | Conditions
CO2 Pressure, MPa | 0.69
Temperature, oC | 90
Chloride Concentration, mg/L | 80,000
Liquid Velocity, m/s | 1.5
Water Cut, % | 100
Duration, hour | 9.5

## Slide 16
Comparison Results Between Weight-Loss Coupons and i-ER Probe
 | Testing Description | Corrosion Rate, mm/yr |  | 
 |  | Weight-Loss Coupon | i-ER Probe | % Difference
Test 1 | Baseline Corrosion | 6.42 | 5.75 | 10.4
Test 2 | Corrosion Inhibitor of 150 ppm | 0.093 | 0.102 | 9.7
i-ER Probe Weight-Loss Coupon
Photos of i-ER Probe and Weight-Loss Coupon After the Flow Loop Test
Liquid Velocity = 1.5 m/s, 150 ppm of corrosion inhibitor
Test Results of i-ER

## Slide 17
Test Results of i-ER
Corrosion Rate Variation of i-ER Probe, Liquid Velocity = 1.5 m/s Baseline (No Corrosion Inhibitor)

## Slide 18
Test Results of MFS
Testing Pipe System
Parameters | Test Conditions
CO2 Pressure, MPa | 6.0
Temperature, oC | 100
Chloride Concentration, mg/L | 160,000
Liquid Velocity, m/s | X
Water Cut, % | 100

## Slide 19
Test Results of MFS
Weight-Loss Coupon
i-ER
PDS
Photos of Weight-Loss Coupon and MFS
After the Test
MFS
General Corrosion Rate | 
Weight-Loss Coupon | 6.58 mm/yr
MFS | 6.02 mm/yr

## Slide 20
Test Results of MFS
i-ER
PDS
Metal Loss
Pit Depth of Weight-Loss Coupon
Maximum Pit Depth | 
Weight-Loss Coupon | 65.84 µm
MFS | 75 µm

## Slide 21
Conclusions
Three corrosion monitoring systems (i-ER probe system, pit-detection probe system and multi-functional probe system) were introduced.
Multi-functional corrosion monitoring system (MFS) is the only system in the world that can measure general and pitting corrosion.
All monitoring systems are designed to be applicable to all environmental conditions in real-time, providing you with the most up-to-date information.
The MFS provides information for the general corrosion rate using i-ER and pitting corrosion using PDS in real-time.
The high-resolution transmitter has a self-diagnosis function regarding abnormal voltage and temperature.

## Slide 22
Reach out.
THANK YOU
email
phone
Calle Cualquiera 123, Cualquier Lugar
JUBCOR
CONFERENCE & EXHIBITION
2024
INNOVATIVE SOLUTIONS FOR CORROSION CHALLENGES
+1-614-401-9667
ck@nexcorr.com